## Slide 1: Automatic Tea Steeper Contraption Design Overview
Design by Tom Dunbar

## Slide 2
This is a design for an automatic tea steeping contraption that is gravity powered and steeps a tea bag for approximately 5 minutes. After the steeping is complete, a bell is rung one time and the tea bag is lifted from the water. The contraption is based around a flying pendulum escapement so it contains no gears, despite it essentially being a clock.
The contraption was inspired by this delightfully over-engineered tea temperature monitoring mechanism: https://www.youtube.com/watch?v=oJzy1vk2zyc&list=PLxYRkul9JZoOfj6--7C8BmSLWSMhE7KK8&index=25&pp=gAQBiAQB
From this video, I liked the notification mechanism so much, I incorporated it into my design. I also like the aesthetic and functionality of the Kontax Stirling engine (https://stirlingengine.co.uk/products/KS90R-Ross-yoke-Aluminium-Stirling-Engine-p593670073), so I used some parts of it in the design. The goal is to create something that would look at home in a Victorian inventor’s parlor. As such, I did not want to use any electronics and wanted to use a ‘natural’ energy source e.g. gravity or the heat from the hot water.

## Slide 3: Main Mechanism Overview
The mechanism works by gravity pulling the weight down, pulling on the string (blue).
The string is wrapped around a main vertical shaft and a drum. The drum is on a horizontal shaft with a wheel. As the string is played out, it causes the main vertical shaft to rotate as well as the drum/wheel to rotate.
The main shaft has a flying pendulum escapement to slow the weight’s decent.
A tea bag’s string is attached to a peg on the wheel and a mug of hot water is positioned below the wheel. As the wheel rotates, it slowly steeps the tea bag up and down.
As discussed later, after 5 minutes there is a steeping complete notification that rings a bell one time to alert the tea drinker that the tea is ready, similar to the notification in the inspiration video. The mechanism also lifts the tea bag out of the water.

## Slide 4: Flying Pendulum Escapement
The link below is a good introduction to a flying pendulum and discusses some of the critical dimensions:
https://www.youtube.com/watch?v=z8V6RMJbHJc
The link below provides some good technical drawings of the escapement and some of the dimensions are visible in the PDF that you can view online. I used some of these dimensions when designing the device.
https://www.woodenclocks.co.uk/clock-17/
The following video is a bit long, but provided the original a-ha moment for how to actually accomplish the auto-steeping mechanism. The main mechanism is essentially a re-arrangement of his contraption:
https://www.youtube.com/watch?v=uuelh5Yt9-Q

## Slide 5: Sub Assembles
Main pillar and Support
Upper static arms
Lower static arms
Rotating assembly
Wheel & Drum
Steeping complete notification contraption
Wooden Base

## Slide 6
A slight offset (~10 degrees) between the upper and lower arms allows the string the disengage cleanly and helps it engage on the upper arm first when it swings around.
In this view, the pendulum is rotating counter-clockwise.

## Slide 7: Resetting the device
To reset the device, the flying pendulum bob is placed onto the wire hook that is on the pendulum arm. This allows the user to spin the crank without the pendulum bob wrapping around the static arms. This will wind up the string and prepare the weight for its next decent.
The pendulum bob is then looped over the upper static arm support beam to prevent the pendulum arm from moving (as seen in this video: https://www.youtube.com/watch?v=z8V6RMJbHJc)
When the pendulum is prevented from moving, the user can attach a tea bag’s string to the peg on the wheel and prepare a mug of hot water.
Un-looping the pendulum bob and letting go is all that is needed to start the main mechanism.

## Slide 9: Wheel and drum
Wheel is inspired by the Kontax Stirling Engine wheel
The tea bag’s string is held by the slot on the peg

## Slide 10: Steeping Complete Notification Contraption
This contraption is designed to strike a bell one time when steeping is complete, after approximately 5 minutes.
The weight descends until it starts to rest on the platform. When the weight puts a small amount of force on the platform, a track pivots and a ball bearing (or marble) rolls down the track. The ball bearing strikes the bell and is caught in a shallow dish.
The shallow dish is separate from the rest of the mechanism so it can be easily repositioned as necessary to catch the ball. It will likely include some padding to help catch the ball. If necessary, a small magnet can be placed under the padding to help retain the ball bearing.
The inspiration for the bell notification mechanism came from video below. The whole video is worth watching, but skip to 19:30 if you just want to see the bell mechanism.
https://www.youtube.com/watch?v=oJzy1vk2zyc&list=PLxYRkul9JZoOfj6--7C8BmSLWSMhE7KK8&index=25&pp=gAQBiAQB

## Slide 13: Tea Bag Lifter Mechanism
Attached to the back of the ball track is a bent rod that is the tea bag lifter mechanism
When the ball track rotates, the rod will rotate up, lifting the tea bag out of the mug
Tea Bag
Mug

## Slide 14: Wooden Base
Red Morrel Burl - https://www.youtube.com/watch?v=vFXsJNO3qsI
Curly Koa is another good wood for a base
But Walnut trophy bases are much less expensive:
  https://www.jpplus.com/solid-walnut-plaque-base?sku=XP5114-EA
  https://www.jpplus.com/roman-cove-edge-plaque?sku=W791-EA

## Slide 15: Tea Organizer base
In order to have enough room for a mug underneath the wheel, I think the device might need to be placed on a stand like this tea organizer.
Alternatively , this type of chest/organizer could be built into the wooden base. It would be much more elegant this way, though difficult to find an artisan who can make a nice chest and do the machining.

## Slide 16: String and Weight
https://www.amazon.com/Slotted-Weight-Set-100g-Removable/dp/B08JM71KVX

## Slide 17: Parameters influencing steeping time
Length of main weight travel
  Design goal: ~300 mm
Seconds per rev (s/rev)
  Design goal: ≥ 9 sec/rev
  Pendulum string length has the largest influence on this parameter
  Other factors include:
    Pendulum weight
    Mass of main weight
    Distance between static arms (?)
    Angle between upper and lower static arms
    Friction
String extended per rev (mm/rev)
  Diameter of rotating rod (3mm)
  Diameter * π